## Slide 1
Design of an Integrated Modular Motor Drive (IMMD) for Traction Applications
Thesis Supervision Committee
Mesut Uğur
Department of Electrical and Electronics Engineering
Middle East Technical University
26.12.2018
Supervisor: Asst. Prof. Dr. Ozan Keysan

## Slide 2
Outline
Thesis Topic
Research Opportunities
Master Plan
Research Work
Prototype Implementation
Test Results
Future plan

## Slide 3
Thesis Topic
Integrated Modular Motor Drive
The motor drive is integrated to the motor
Both the motor and the drive are modularized
Increased power density
Reduced cost
Reduced EMI
Fault tolerance
Redundancy
Reduced stress
Brown, N. R., Jahns, T. M., & Lorenz, R. D. (2007). Power Converter Design for an Integrated Modular Motor Drive. Industry Applications Conference, 2007. 42nd IAS Annual Meeting. Conference Record of the 2007 IEEE, 1322–1328.
Applications
Mission or safety critical applicaitions
Size, volume or weight constraints
Challenges
Size reduction
Thermal management
Vibration
Shea, A., & Jahns, T. M. (2014). Hardware integration for an integrated modular motor drive including distributed control. In 2014 IEEE Energy Conversion Congress and Exposition (ECCE) (pp. 4881–4887). IEEE.

## Slide 4
Research Opportunities
Wide Band-Gap Power Semiconductor Devices: GaN FETs
Layout design, parasitics modeling and minimization
Size reduction, passive component design and optimization
Modular motor drive topologies, fault tolerance, interleaving
Fault tolerant operation of machines, fault detection and re-action
Permanent magnet motor design and optimization
Vibration effects and minimization
Thermal management of two heat sources in close proximity
Filter design with planar magnetics

## Slide 5
Master Plan
Two IMMD prototypes
A proof of concept prototype with:
  Utilization of GaN FETs at 8 kW
  Modular design with 2-series and 2-parallel connected inverters
  Permanent magnet synchronous machine
  Different windings configurations (fractional slot concentrated winding)
  Fault detection, analysis and operation under fault
  Going through all the design, manufacturing, assembling and testing procedures
An IMMD prototype for an aerospace or traction application
  Aircraft fuel pump
  In-wheel motor
  etc.

## Slide 6
Research Work
Design of the 8 kW IMMD system: Drive parameters
Parameter | Value
Motor output power, Pout | 8 kW
DC link voltage, Vdc | 540 V
Number of phases, m | 3
Power factor, pf | 0.9
Motor speed, Nr | 600 rpm
Parameter | Value | Parameter | Value
Type | E-mode GaN | Manufacturer | GaN Systems
Voltage | 650 V | Current (25 0C) | 30 A
Rds,on (25 0C) | 50 mΩ | Rds,on (150 0C) | 129 mΩ
Rise time | 4.9 ns | Fall time | 3.4 ns
Turn-on energy | 47.5 µJ | Turn-off energy | 7.5 µJ

## Slide 7
Research Work
Design of the 8 kW IMMD system: Motor parameters
Parameter | Value | Parameter | Value
Stator slot number, Qs | 24 | Air gap length, lg | 1.5 mm
Rotor pole number, p | 20 | Magnet height, lm | 4.5 mm
Motor axial length, La | 135 mm | Number of turns per coil, zQ | 40
Stator outer diameter, Dos | 270 mm | Slot fill factor, kcu | 0.4
Stator inner diameter, Dis | 180 mm | Stator winding factor, kw | 0.933

## Slide 8
Research Work
Design of the 8 kW IMMD system: Capacitor & interleaving
Parametre | Value
Capacitor current (RMS), Ic,rms | 5.76 A
Capacitance, Cdc | 18 µF
Capacitor voltage, Vc | 300 V
Total number of capacitors | 2

## Slide 9
Research Work
Topology Evaluation
Efficiency vs Switching frequency
Power loss components
Conventional
Parallel
Series

## Slide 10
Research Work
GaN Modeling: Steady-state and transient models
Forward characteristics
Reverse characteristics
Temperature effect
Capacitance model

## Slide 11
Research Work
GaN Modeling: Switching characteristics
Top
turn-on
Bottom
turn-off
Top
turn-off
Bottom
turn-on

## Slide 12
Research Work
GaN Modeling: Parameter effects
Temperature effect
Load current
RG-on effect
RG-off effect

## Slide 13
Research Work
Motor design: Design procedure and numerical results
Parameter | Value
Induced voltage per phase per module, Eph-m | 78 Vrms
Line current per phase per module, Iph-m | 10 Arms
Motor torque, Tm | 127 Nm
Fill factor, kcu | 38 %
Current density, Jrms | 3.8 A/mm2
Copper loss, Pcu | 229 W
Core loss, Pcore | 96 W
Motor efficiency, ηm | 95.9 %
Electromagnetic model
Slot geometry
Magnet shape
Torque ripple: 0.63 %
Cogging torque: 0.29 %
Inductance: 3.66 mH
This will result in relatively high short circuit current

## Slide 14
Research Work
Motor design: FEA results
Motor torque
Induced voltages

## Slide 15
Research Work
Motor design: FEA results
Line currents
Flux density distribution

## Slide 16
Prototype Implementation
IMMD system design: Architecture

## Slide 17
Prototype Implementation
Motor drive inverter PCB design

## Slide 18
Prototype Implementation
Motor drive inverter PCB design

## Slide 19
Prototype Implementation
Parasitic modeling: Inductance and resistance
ANSYS/Q3D Extractor
Inductance map of the PCB
Effect of inductances on capacitor RMS current

## Slide 20
Prototype Implementation
Control PCB design: Schematic
Power supply (Flyback converter)
DC Link distribution
Interchangable DC link connections
Micro-controller (DSP) circuit
JTAG interface
Communication interface
DC link voltage measurement
ADC filters, PWM circuits etc.

## Slide 21
Prototype Implementation
Control PCB design: Layout

## Slide 22
Prototype Implementation
Control PCB design: 3D view

## Slide 23
Prototype Implementation
Motor manufacturing

## Slide 24
Prototype Implementation
Thermal design: Lumped parameter network
Parameter | Value | Parameter | Value
Ambient temperature | 40 0C | PCB thermal resistance | 3.39 0C/W
Junction temperature | 140 0C | TIM thermal resistance | 0.13 0C/W
Power loss | 7 W | Junction-to-case thermal resistance | 0.5 0C/W

## Slide 25
Prototype Implementation
Thermal design: Analysis
Operating point
Analytical calculation of convection coefficient (natural & forced)
h = 5.1 W/m-K for natural convection
h = 18.4 W/m-K for forced convection (1 m/s air flow)
Lumped parameter thermal network simulation:
Required Rth_hs = 1 0C/W

## Slide 26
Prototype Implementation
Thermal design: Heat sink & thermal tests

## Slide 27
Prototype Implementation
Thermal design: Finite element Analysis
Loss: 10W per GaN
Ambient: 40 0C
Convection coefficienct: 18 𝑊/(𝑚−𝐾)
Junction: 109 0C

## Slide 28
Prototype Implementation
Thermal design: Finite element Analysis
Loss: 10W per GaN
Ambient: 40 0C
Convection coefficienct: 5 𝑊/(𝑚−𝐾)
Junction: 151 0C

## Slide 29
Prototype Implementation
Mechanical design: Overall system

## Slide 30
Prototype Implementation
Mechanical design

## Slide 31
Experimental Results
Motor Drive Tests: Experimental setup
Rectifier & DC Bus
Resistive & inductive loads
DSP board
Inverter module
Probes
DC & AC wattmeters
500 MHz oscilloscope
Power supply

## Slide 32
Experimental Results
Motor Drive Tests: Test plan
PCB functional tests ✔
Gate driver tests ✔
Test 0: Double pulse test (DPT) @ 100V, 10A ✔
Test 1: No load, Vdc = 100 V, fsw = 40 kHz ✔
Test 2: 60 W , Vdc = 100 V, fsw = 10 kHz ✔
Test 3: 300 W , Vdc = 100 V, fsw = 10 kHz ✔
Test 3.5: Double pulse test (DPT) applied to each phase @ 270V, 20A
Test 4: 410 W , Vdc = 270 V, fsw = 10 kHz
Test 5: 2000 W, Vdc = 270 V, fsw = 10 kHz
Test 6: 2000 W, Vdc = 270 V, fsw = 40 kHz

## Slide 33
Experimental Results
Motor Drive Tests: Results
Double pulse test
Square wave operation
3-phase sinusoidal PWM
Configurable magnitude, frequency, dead-band etc.
Gate-source waveforms
Turn-on
Turn-off

## Slide 34
Experimental Results
Motor Drive Tests: Double pulse test
During DPT, one GaN FET is lost (gate driver zener diode is destroyed)
Load current

## Slide 35
Experimental Results
Motor Drive Tests: Test-3 Results
Line-to-line voltage
Line currents

## Slide 36
Experimental Results
Motor Drive Tests: Test-3 Results
During low voltage (100V) test, one GaN is lost due to experimental setup grounding

## Slide 37
Experimental Results
Motor Drive Tests: Test-4
During high voltage (270V) test, four GaNs are lost at 225V:
1. Voltage clearance: Clearance test is performed up to 560V between all possible nodes. PCB passed this test.
2. Voltage breakdown due to overshoot: Still under investigation. Tests are applied in DPT mode up to 300V and results suggest that there is no overshoot problem.

## Slide 38
Experimental Results
Motor Drive Tests: Results of DPT applied to each phase
Phase-B
Phase-A
Phase-C
All-phases

## Slide 39
Experimental Results
Motor Drive Tests: Results of DPT applied to each phase

## Slide 40
Future plan
What is ahead: Short term
Continue with inverter tests, figure out and solve the problem
Assemble 3 more motor drive module PCBs and test them
Assemble control board and test it
Test the motor drive module on a motor
Assemble the control PCB and motor drive modules altogether
Manufacture the remaining motor and mechanical parts
Assemble the motor
Test the motor parameters
Drive the motor with a commercial drive to see its performance
Assemble the IMMD altogether (drive + motor)
Test the IMMD system
Fault tolerance tests

## Slide 41
Future plan
What is ahead: Long term

## Slide 42
Publications
DC Link Capacitor Optimization for Integrated Modular Motor Drives
IEEE 26th International Symposium on Industrial Electronics (ISIE 2017)
Tümleşik Modüler Motor Sürücü Sistemi Tasarımı
1. Ulusal Enerji Dönüşümü Kongresi (EL-EN 2017)-Fırat Üniversitesi Mühendislik Bilimleri Dergisi
Multi-physics design optimization of a GaN based integrated modular motor drive system
The 9th International Conference on Power Electronics, Machines and Drives (PEMD 2018)
Investigation of Turn-on and Turn-off Characteristics of Enhancement-Mode GaN Power Transistors
20th European Conference on Power Electronics and Applications (Energy Conversion Conference and Exhibition) (EPE 2018)
Comparison of Inverter Topologies Suited for Integrated Modular Motor Drive Applications
18th International Conference on Power Electronics and Motion Control (PEMC 2018)
Design of a GaN Based Integrated Modular Motor Drive
The International Conference on Electrical Machines (ICEM 2018)

## Slide 43
References
Brown, N. R., Jahns, T. M., & Lorenz, R. D. (2007). Power Converter Design for an Integrated Modular Motor Drive. Industry Applications Conference, 2007. 42nd IAS Annual Meeting. Conference Record of the 2007 IEEE, 1322–1328.
Shea, A., & Jahns, T. M. (2014). Hardware integration for an integrated modular motor drive including distributed control. In 2014 IEEE Energy Conversion Congress and Exposition (ECCE) (pp. 4881–4887). IEEE.
Marz, M., Schletz, A., Eckardt, B., Egelkraut, S., & Rauh, H. (2010). Power electronics system integration for electric and hybrid vehicles. Integrated Power Electronics Systems (CIPS), 2010 6th International Conference On, 16–18.
Wheeler, P. W., Clare, J. C., Apap, M., Empringham, L., Bradley, K. J., Pickering, S., & Lampard, D. (2005). A fully integrated 30 kW motor drive using matrix converter technology. Proc. EPE ’05, 9, 9–16.
Wang, J., Li, Y., & Han, Y. (2013). Evaluation and design for an integrated modular motor drive (IMMD) with GaN devices. 2013 IEEE Energy Conversion Congress and Exposition, ECCE 2013, (Immd), 4318–4325
Wang, J., Li, Y., & Han, Y. (2015). Integrated Modular Motor Drive Design With GaN Power FETs. IEEE Transactions on Industry Applications, 51(4), 3198–3207.
Lee, W., Li, S., Han, D., Sarlioglu, B., Minav, T. A., & Pietola, M. (2017). Achieving high-performance electrified actuation system with integrated motor drive and wide bandgap power electronics. In 2017 19th European Conference on Power Electronics and Applications (EPE’17 ECCE Europe) (p. P.1-P.10). IEEE

## Slide 44
Thank you !
Mesut Uğur
mesut.ugur@metu.edu.tr
Department of Electrical and Electronics Engineering
Middle East Technical University
power.eee.metu.edu.tr