## Slide 1
Complete System Modeling
for
Integrated Modular Motor Drive
Mesut Uğur
14/10/2019
mesut.ugur@metu.edu.tr

## Slide 2
Content
Simplest inverter model
Parasitics added
Unbalance on load
Rectifier added
2-parallel with and without interleaving
2-parallel – parasitics added
2-parallel – load and module unbalance
2-parallel – rectifier added
2-series with and without interleaving
2-series – parasitics added
2-series – load and module unbalance
2-series – rectifier added

## Slide 3
Simplest inverter model
Single module 3-phase inverter
Load is balanced RL load
DC bus is ideal current source
DC bus input current is almost DC
No LF harmonic injection from input
No HF harmonic flow from output
Isa
Isb
Isc
Idc
Vdc
Iin
Vin
Vab
Vbc
SA, SB, SC
Sinusoidal PWM – fsw = 10kHz
Generic parameters: pf = 0.9, ma = 0.9
270Vdc, 2kW system
Iin = 7.4A, Icaprms = 4.8A, Vdcrip = 6% (15uF), Isrms = 8.6A
Iin ripple is made 4% (almost DC)

## Slide 4
Simplest inverter model
Isa, Isb, Isc
Idc = SAIsa + SBIsb + SCIsc
SA, SB and SC can currently be modeled in all aspects. We also have an analytical model.
Using the Sx models, Isx models can easily be obtained.
Using these two, Idc is also obtained analytically, which is good.
When parasitics inside the PCB are ignored, we can assume that Idc is not affected (as a model) by input side (input current, rectifier etc.)
Existance of parasitics is another matter, see the next section.
This looks like 300 Hz ripple, well, it is not 
See next slides.
Low harmonic content in Isx’s is due to large inductive load.

## Slide 5
Simplest inverter model
Iin
Vdc
This looks like 300 Hz ripple, well, it is not 
See next slides.
This is intentionally made almost DC, trying to exert all the ripple content to capacitors. It is achieved by putting a large resistor to input.
Vdc ripple content is ideally obtained with simple capacitor equation (voltage is integral of current).
When ESR and ESL are considered, this model is more complex, which is not modeled here.
Practically, there are three capacitors which have parasitics in between, making the analysis way more complex.
Therefore these effects are not considered in this simplest model.

## Slide 6
Simplest inverter model
SA - Around fsw
SA - Around 2*fsw
SA harmonics are due to the nature of PWM and can be manipulated (not in the scope of this study right now.)
Some harmonics are 120 degrees apart in 3 phases (SA,SB,SC), some are inphase.
When currents are balanced, 120 degrees apart harmonics cancel in the multiplication in Idc formula. Only inphase component are reflected to the DC bus.
These are analytically modeled by @EnesAyaz!
 | SA |  | SB |  | SC | 
Freq | Mag(%) | Phase(deg) | Mag(%) | Phase(deg) | Mag(%) | Phase(deg)
9900 | 27 | 90 | 27 | -30 | 27 | 210
10000 | 71 | 90 | 72 | 90 | 72 | 90
10100 | 27 | 90 | 27 | 210 | 27 | -30
19850 | 18 | 0 | 18 | 0 | 18 | 0
19950 | 25 | 0 | 25 | 120 | 25 | 240
20050 | 25 | 180 | 25 | 60 | 25 | -60
20150 | 18 | 180 | 18 | 180 | 18 | 180

## Slide 7
Simplest inverter model
Isa - Around fsw
Isa - Around 2*fsw
Due to wye connection (?), the inphase components of Sx harmonics are not seen in phase currents.
Again, these are under balanced conditions. Unbalance will be analyzed separately.
All the current harmonics are 120 degrees apart.
Their magnitudes and phase depend on load angle, Vdc, load values etc.
 | Isa |  | Isb |  | Isc | 
Freq | Mag(%) | Phase(deg) | Mag(%) | Phase(deg) | Mag(%) | Phase(deg)
9900 | 0.34 | -2 | 0.34 | 238 | 0.34 | 118
10000 | 0 |  | 0 |  | 0 | 
10100 | 0.34 | -2 | 0.34 | 118 | 27 | 238
19850 | 0 |  | 0 |  | 0 | 
19950 | 0.16 | 264 | 0.16 | 24 | 25 | 144
20050 | 0.16 | 84 | 0.16 | -36 | 25 | 204
20150 | 0 |  | 0 |  | 0 | 

## Slide 8
Simplest inverter model
Idc - Around fsw
Idc - Around 2*fsw
Idc is formed by the the sum of the multiplication Sx and Isx of each phase. This multiplication creates new harmonic frequencies by the trigonometric rules ((x+y) and (x-y)) .
Most of these components, under balanced conditions cancel out because of the 120 degrees apart form. Only the in-phase components remain which are multiplied by the large DC and fundamental components of Sx and Isx.
Also, some frequencies are shifted by 50 Hz due to multiplication with fundamental. All in all, we have the following remaining:
 | Idc | 
Freq | Mag(%) | Phase(deg)
9900 | 32 | 204
10000 | 0 | 
10100 | 33 | -32
19850 | 0 | 
19950 | 0 | 
20000 | 56 | 263
20050 | 0 | 
20150 | 0 | 
A more detailed explanation can be given by the analytical model (which is in many pages )

## Slide 9
Simplest inverter model
Envelope phenomenon
We have seen that there are two sideband harmonics near switching frequency: 9850 Hz & 10150 Hz.
They can be expressed as: A sin(2π9850t + φ1) + A sin(2π10150t + φ2)
They can also be rewritten as: 2A sin(2π10000t + (φ1 + φ2)/2) sin(2π150t + (φ1- φ2)/2)
The same harmonic content can be represented with the multiplication two components which are: fsw and 3xfo. The 150 Hz is therefore seen as an envelope.
All in all, there is no actual low order (300 Hz etc.) harmonic injection from the inverter to the DC bus provided that the load is balanced.
Envelope

## Slide 10
Simplest inverter model
Idc harmonics are directly injected to Icap (well, almost…). Therefore, their presence on the DC bus voltage is also directly reflected.
Magnitudes are determined by switching frequency and capacitance.
Of course, phase of those harmonics change, which will be important in interleaving studies.
Same envelope phenomenon is seen here.
Vdc - Around fsw
Envelope

## Slide 11
Simplest inverter model
Here, a 150Hz and a 10000Hz source are multiplied.
Envelope is shown above.
The harmonic content is shown on the left.
9850Hz & 1150Hz are dominant.
Actually, this is the reverse of what we have.
We may (and will) use this for DC bus bulky capacitor size reduction in the future !
More about envelope

## Slide 12
Parasitics added model
Inner power loop consists of seramic capacitors and handles the switching oscillation (in the order of 100MHz). It is directly related to the device Vds breakdown (out of scope).
Outer power loop consists of the large film capacitor (5 uF each). It is the loop where the switching harmonics (components of Idc) flow, which is our interest.
In commutation loops, the switching harmonic current flows from one phase to a capacitor belonging to a different phase. Therefore, our «single Idc» assumption fails.
There is a stray inductance between all components, consequently resulting in increase on capacitor stress.

## Slide 13
Parasitics added model
The DC bus design affects the distribution capacitor stress.
Below results are simulation results for the previus inverter (V2)
Below are the test results:

## Slide 14
Parasitics added model
A cleaner result:
RMS comparison:
Note that, test results are obtained by measuring each capacitor voltage, and obtaining their current using integral (ESR, ESL etc. are neglected)

## Slide 15
Parasitics added model
Study on the parasitics added model is still ongoing.
First, the simulation results should be renewed with V1.3 board.
FFT analysis is to applied for a better understanding.
An analytical model using impedance models is developed, still ongoing.

## Slide 16
Rectifier added model
Let us first look at the test results, where rectifier is used.
Here, we see that the input current is not ideal DC. It is composed of:
  Switching frequency harmonics.
  Low order harmonics.
  Unbalanced envelope.
The switching harmonics are due to the fact that the source is not an infinite bus and the bulky capacitor at rectifier output draws some of the high frequency ripple.
The low order harmonics may be of many things: rectifier 6th harmonic, unbalance etc…
Here those phenomena will be examined separately for better understanding.

## Slide 17
Rectifier added model
First, the previously mentioned effect is created by reducing the series Rin resistance so that some harmonics can flow to the input:
Rin
Yellow: Idc
Orange: Iin
Rin = 50 Ohms Rin = 5 Ohms
Iin
Idc

## Slide 18
Rectifier added model
Some of the switching harmonics flow to the input as shown below, when the resistance is decreased.
Rin = 50 Ohms Rin = 5 Ohms
 | Rin = 50 Ohms | Rin = 5 Ohms
Icap-RMS | 4.825 A | 4.795 A
Iin-DC | 7.422 A | 7.435 A
Iin-RMS | 7.423 A | 7.459 A
Idc-DC | 7.422 A | 7.435 A
Idc-RMS | 8.853 A | 8.868 A
Numericly, it seems that it did not make large difference.
Let us look at specific harmonics:
9850 Hz | Rin = 50 Ohms | Rin = 5 Ohms | 20000 Hz | Rin = 50 Ohms | Rin = 5 Ohms
Icap | 2.384 | 2.335 | Icap | 4.178 | 4.162
Iin | 0.051 | 0.503 | Iin | 0.044 | 0.441
Idc | 2.385 | 2.388 | Idc | 4.179 | 4.186

## Slide 19
Rectifier added model
Now, let us add an actual rectifier:
Bulky capacitor
(1.1mF)
Film capacitors
(15uF)
Rmid (Represents cabling etc.)
With small Rmid, the Idc ripple mostly flows through the bulky capacitor since its impedance is 100 times smaller. But, this is not the case as seen from the experimental results. Therefore, Rmid is made 4 Ohms for now and the following result is obtained:

## Slide 20
Rectifier added model
None of these harmonics existed before, as obviously they are due to the nature of 3-phase full-bridge rectifier.
Iin Idc Icap
When compared with the model with small Rin (5 Ohms) and ideal DC source, the results are similar considering high order harmonics (related to switching frequency).
But, one should note that it is not possible to have a 4 Ohms resistor in between the rectifier and inverter. Its loss will be more than 250 Watts alone !!!
This situation is not still clear and should be worked on.
As for the low order harmonics:
Note that this is not percent

## Slide 21
Rectifier added model
When

## Slide 23
Thank you !
mesut.ugur@metu.edu.tr